How to run helium leak check using RGA(Residual gas analyzer).

Aug 2012

Jaseung Ku

- Pump down a system to at least 2x10-4 Torr.

- Open the valve between the RGA and pump system.

- Connect the RS-232 cable to computer through USB port.

- Run RGA software.

- Click   Head -> Connector List Setup.

- Select RGA instrument and click Connect.

- Click  Head -> Filament On(to turn on the filament).

- Click Mode - > Leak Test.

- Click Scan-> Start

- Spray helium gas to the system and see if there is any pressure rise.

Once the leak-check is done,

- Click Scan-> Stop Now.

- Click Head-> Filament On(to turn off the filament).

- Click Head-> Connector List Setup and then Disconnect.

- Close the valve between the RGA and pump system.

- Disconnect the RS-232 cable from the computer.