How to order E-beam writing on a wafer to MNTL

Aug 2011

Jaseung Ku

1. Draw unit cells in Autocad. Set the unit to be micron. (Autocad command: “units”)

Remarks:

a. Set the center of unit cell as an origin (0,0).

b. Orient trench lines horizontally.

c. If different trench width is necessary, make a unit cell that contains the trench line only. This allows us to change the trench ( length, number of trench, etc.)

2. Draw a whole pattern by inserting unit cells. Use “array” to duplicate the unit cells.

3. Save as 2000/LT2000 dxf

4. Convert the file to GDS using Linkcad in Raith file prep room or other softwares.

Remark : DO NOT flatten the structures.

5. Send the following :

a) GDS file

b) Description of ALL layers

c) Layer numbers to be exposed

d)(recommended) simple diagram of wafer structure

Example :  Layer 0=trench, Layer 1=NumberMarker, Layer 2=CornerMarker, Layer 3=Outline. Please expose Layer 0, 1 and 2.

6. Drop off a wafer to the staff.